## Slide 1: Physical Layer
School of Computer Science Engineering and Technology Bennett University
Greater Noida – 201310

## Slide 2: Physical Layer

## Slide 3: Physical Layer
The physical layer is the lowest layer of the OSI
model.
This layer controls the way unstructured, raw, bit - stream data is sent and received over a physical medium.
This layer is composed of the electrical, optical, and physical components of the network.
It carries the signals for all of the higher layers.
This layer plays with most of the network’s physical
connections -
wireless transmission, cabling, cabling
standards and types, connectors and types, network
interface cards
, and more - as per network
requirements.

## Slide 4: Outline
Physical Layer: Services
Line coding
Modulation
Multiplexing
Switching

## Slide 5: Physical Layer: Services
Representation of Bits: Data in this layer consists of stream of bits. The bits must be encoded into signals for transmission. It defines the type of encoding i.e., how 0's and 1's are changed to signal.
Data Rate: This layer defines the rate of transmission which is the number of bits per second.
Synchronization: The sender and receiver are synchronized at bit level.
Interface: Transmission interface between devices and transmission medium.
Line Configuration: Point to Point configuration and Multipoint configuration.
Network topologies: Mesh, Star, Ring, Bus, Tree, and Hybrid.
Transmission Modes: Simplex, Half Duplex, Full Duplex.
Deals with baseband and broadband transmission.

## Slide 6: Line coding
Line coding – Conversion of digital data to digital signal.
Sender converts sequence to bits (or encoding) into a digital signal which then again converted into bits (or decoded) by the receiver.

## Slide 7: Line coding: Relationship between data and signal
𝑆 = 𝑐𝑁 baud
𝑟
where S = baud rate, c = case factor, N = bit rate, r is the ratio of data element carried by each signal
Data elements are being carried whereas signal elements are the carriers.
The number of data elements sent per second is known as bit rate.
The signal that can be sent per second is known as baud rate or pulse rate.
The relationship between them is given as follows:

## Slide 8: Line coding: Relationship between data and signal
E.g.- A signal is carrying data in which one data element is encoded as one signal element (r = 1). If bit rate is 1 Mbps and case factor c is ½ (in most of the cases) then what will the value of baud rate?
Sol: S = 1/2 * 1000000 * 1/1 = 500 kbaud

## Slide 9: Line coding: Schemes

## Slide 10: Line coding: Unipolar
It uses only one voltage level.
It is also called On-Off Keying or simply OOK.
Positive voltage is defined by bit 1 and zero voltage defines bit 0.
Two variations:
  Non-Return-to-Zero (NRZ): Signal does not return to zero at the middle of the bit.
  Return to Zero (RZ): Signal returns to zero at the middle of the bit.

## Slide 11: Line coding: Unipolar
Unipolar Non-Return to Zero (NRZ)
A High (1) in data is represented by a positive
pulse.
A Low(0) in data input has no pulse.
Unipolar Return to Zero (RZ)
A High in data represented by a +ve pulse but its duration is
less than the symbol bit duration.
Half of the bit duration remains high, but it immediately returns to zero and shows the absence of pulse for remaining half.

## Slide 12: Line coding: Polar
It uses two voltage levels – one positive and the other one negative.
The voltages are on both sides of the time axis.
Binary values; 0 and 1, are used to show +ve and –ve voltage, respectively.

## Slide 13: Polar: NRZ
The signal level remains same throughout the bit-period.
Two encoding schemes:
  NRZ Level (NRZ-L)
  NRZ Inverted (NRZ-I)
NRZ-L
1 = Low level
0 = High level
NRZ-I
For each 1 in the bit sequence, the signal level inverted.

## Slide 14: Polar: RZ
RZ scheme uses three values: positive, negative, and zero.
In RZ, the signal changes not between bits but during the bit.
The signal goes to 0 in the middle of each bit, and it remains there until the beginning of the next bit.

## Slide 15: Polar:Manchester Manchester

## Slide 16: Polar:Diffrential Manchester Manchester

## Slide 17: Line Coding: Bipolar
It is also called as multilevel binary scheme.
It is of two types:
  Alternate Mark Inversion (AMI): A neutral zero voltage represents binary 0 whereas binary 1s (Mark) are represented by alternating +ve and –ve voltages.
  Pseudoternary: Binary 1 bit is encoded as a zero voltage and the binary 0s are represented by
alternating +ve and –ve voltages.

## Slide 18: Line coding: Bipolar
AMI
Pseudoternary

## Slide 19: Line Coding Self Practice Example
Encode the bit stream 000111101011 using
  Unipolar
  NRZ-L
  NRZ-I
  Manchester
  Differential Manchester
  AMI
  Pseudoternary

## Slide 20: Switching
A process to forward packets coming in from one port to a port leading towards the destination
Two terms used
  Ingress – Data comes on a port
  Egress – Data leaves a port or goes out
Switching can be divided into two categories:
  Connectionless: Data is forwarded on behalf of forwarding table and no manual intervention. It is not secure
  Connection-oriented: A circuit is pre-established along with the path between both endpoints. Data is forwarded on the
circuit and the circuit can be kept for future use or can be turned down immediately.

## Slide 21: Switching : Techniques

## Slide 22: Switching : Circuit Switching
A dedicated path is established between sender and receiver and will remain to exist until the
connection is terminated.
Circuit switching in a network operates in a similar way as the telephone works.
A complete end-to-end path must exist before the communication takes place.
Circuit switching has 3 phases:
  Circuit establishment
  Data transfer
  Circuit Disconnect

## Slide 23: Switching : Message Switching
Message is transferred as a complete unit and forwarded using store and forward mechanism.
No dedicated path is established between the sender and receiver.
The destination address is appended to the message and is routed efficiently using dynamic path.
Each node stores the entire message and then forward it to the next node.
Not suited for streaming media and real-time application.

## Slide 24: Switching : Packet Switching
Message is broken into individual chunk called as packets that is sent individually in the network.
Every packet contains some information in its headers such as source address, destination address
and sequence number.
Packets will travel across the network, taking the shortest path as possible.
Sequence number helps the receiver to reorder the packets, detect missing packets, and send acknowledgement.

## Slide 25: References
https://circuitglobe.com/difference-between-circuit-switching-and-packet-switching.html
https://www.javatpoint.com/computer-network-switching-techniques
https://www.studytonight.com/computer-networks/multiplexing-in-computer-networks
https://www.javatpoint.com/multiplexing-in-computer-network
https://data-flair.training/blogs/multiplexing-in-computer-network/
https://www.youtube.com/watch?v=-HlJ4psu5aU&t=350s
https://www.youtube.com/watch?v=mHvV_Tv8HDQ